## Slide 1: Asynchronous Sequential Circuits

## Slide 2: Asynch. vs. Synch.
  Asynchronous circuits don’t use clock pulses
    State transitions by changes in inputs
  Storage Elements:
    Clockless storage elements or
    Delay elements
  In many cases, as combinational feedback
     Normally much harder to design

## Slide 3: Asynch. Sequential Circuit
delay
delay
delay
Combinational
Circuit
x1
x2
xn
z1
z2
zm
y1
y2
yk
Y1
Y2
Yk
inputs
outputs
Current
State
Next
State

## Slide 4: Asynch. Sequential Circuit
  yi = Yi in steady state (but may be different during transition)
  Simultaneous change in two (or more) inputs is prohibited.
    The time between two changes must be greater than the time of stability.

## Slide 5: Advantages and Disadvantages
Advantages:
  Low power
  High performance
  No need for clock
Disadvantages:
  Complexity of design process

## Slide 6: Analysis
  Find feedback loops and name feedback variables appropriately.
  Find boolean expressions of Yi’s in terms of yi’s and inputs.
Y2
Y1
x
y2
y1
Y1 = x.y1 + x’.y2
Y2 = x.y1’ + x’.y2

## Slide 7: Analysis
  Draw a map:
    rows: yi’s
    columns: inputs
    entries: Yi’s
Y1 = x.y1 + x’.y2
y1 y2
x
00
01
11
10
0
1
0
1
0
0
0
1
1
1
Y2 = x.y1’ + x’.y2
y1 y2
x
00
01
11
10
0
1
0
1
1
1
0
1
0
0
(Transition Table) Y1 Y2
y1 y2
x
00
01
11
10
0
1
00
11
01
01
00
11
10
10
Y2
Y1
x
y2
y1

## Slide 8: Analysis
  To have a stable state, Y must be = y (circled)
(Transition Table) Y1 Y2
y1 y2
x
00
01
11
10
0
1
00
11
01
01
00
11
10
10
  At y1y2x = 000, if x: 0  1
    then Y1Y2: 00  01
    then y1y2 = 01 (2nd row): stable

## Slide 9: Analysis
y1 y2
x
00
01
11
10
0
1
00
11
01
01
00
11
10
10
  In general, if an input takes the circuit to an unstable state, yi’s change until a stable state is found.
  General state of circuit:
    y1y2x:
      There are 4 stable states:
        000, 011, 110, 101
      and 4 unstable states.

## Slide 10: State Table
  As synchronous:
00 01
11 01
00 10
11 10
00
01
10
11
present state
next state

## Slide 11: Flow Table
  As Transition Table (but with symbolic states):
x
a
b
c
d
0
1
a
c
b
b
a
c
d
d

## Slide 12: Flow Table: Example 2
a
b
,0
a
a
,0
a
,0
a
,0
a
,0
b
,1
b
,0
b
,0
x1 x2
00
01
11
10
  Two states, two inputs, one output.
  Each row has more than one stable state.
  If x1 = 0, state is a.
  If x1x2 = 00  x1x2 = 10, then state becomes b.
  For x1x2 = 11, state is either a or b.
    If previously in x1x2 = 01, keeps state a,
    If previously in x1x2 = 10, keeps state b.
    Reminder: cannot go from 00 to 11.

## Slide 13: Circuit Design
  From flow table to circuit:
    Assign a unique binary value to each state,
a
b
,0
a
a
,0
a
,0
a
,0
a
,0
b
,1
b
,0
b
,0
x1 x2
00
01
11
10
0
1
,0
0
0
,0
0
,0
0
,0
0
,0
1
,1
1
,0
1
,0
x1 x2
00
01
11
10
y
x1 x2
1
0
0
0
0
0
0
1
0
0
00
01
11
10
y
  Map for output z (=x1x2y)
0
1
0
0
0
0
0
1
1
1
x1 x2
00
01
11
10
y
  Map for Y (=x1x2’+x1y)

## Slide 14: Circuit Diagram
Y
x1
y
x2
  z = x1x2y
  Y = x1x2’+x1y

## Slide 15: Race Condition
  If two (or more) state variables change in response to a change in an input, there is a race condition.
    E.g. from 00 to 11, due to delays
      00  01  11 OR
      00  10  11.
Critical Race:
  If final steady state depends on the order of changes in state vars.

## Slide 16: Race: Examples
Noncritical Cases:
x
00
01
11
10
0
1
00
11
11
11
11
y1y2
00  11
00  01  11
00  10  11
x
00
01
11
10
0
1
00
11
01
01
11
y1y2
00  01
00  11  01
00  10  11  01

## Slide 17: Race: Examples
Critical Cases:
x
00
01
11
10
0
1
00
11
11
11
10
y1y2
00  11
00  01  11
00  10
x
00
01
11
10
0
1
00
11
01
11
10
y1y2
00  11
00  01
00  10

## Slide 18: Instability
  Y = (x1 y)’ x2
Y
x1
y
x2
0
1
0
1
x1 x2
00
01
11
10
y
1
0
0
0
0
1
  For x1x2 = 11, there is no steady state.
     Oscillation.
  For x1x2 = 11, Y = y’  unstable.

## Slide 19: THE END

## Slide 20: No-Race State Assignment
  Must assign binary values to states such that:
    one change in an input may not cause two changes in state variables.
      because, due to delays, one of the variable change sooner and may stay in an unwanted stable state.
    From a, if x1x2 = 10  11, must go to c and stay there.
    But by the following assignment, it may go to b and stay there.
a
b
a
b
x1 x2
00
01
11
10
c
a
a
b
c
b
c
a
c
c
c
a
b
c
  a and b must be different in one bit,
  a and c must be different in one bit.
00
01
11

## Slide 21: No-Race State Assignment
  Impossible  add one more row.
a
b
a
b
x1 x2
00
01
11
10
d
a
a
b
c
b
c
c
c
c
a
b
c
00
01
11
d
c
d
10
d
a
-
-
  d is an intermediate (unstable) state.
  - means any value can be assigned (Except d=10).

## Slide 22: Example 2
  If there were no diagonal transition, it would be possible
  Impossible  add some more rows.
a
b
a
b
x1 x2
00
01
11
10
d
a
a
b
b
c
c
b
c
d
c
a
c
d
d
d
a
b
c
00
01
11
d
10

## Slide 23: Example 2
a
b = 001
a = 000
b
x1 x2
00
01
11
10
e
a
a
b
b
c = 011
c
b
c
g = 010
g
d
f
f
d
d
110
f = 111
d = 101
e = 100
-
-
-
a
-
-
-
-
c
-
c
-
-
d
-
-
a
1
0
b
y1 y2
00
01
11
10
y3
c
g
e
f
0
d
  b is adjacent to a, c, d
  c  a through g
  a  d through e
  d  c through f
a
b
c
00
01
11
d
10